## Slide 1: FPGA for software developers
Miodrag Milanović

## Slide 2: Introduction
Engineer
Hardware and emulation enthusiast
Software developer since year 2000
Software architect at “Levi Nine” Serbia
Worked in C,C++,C# and Java, lately in C++ only
Working on MAME emulation project since 2006
Was leading MAME project since 2012 till 2016

## Slide 3: Why we are here?
Understanding hardware
To be better developer you need to know and understand how computer works.
Best way to understand how something work is to make it.
“Well I am just software developer and I don’t understand electronics…”
We will write hardware as source code and then “compile” hardware.
“Impossible” and “too hard” are just lame excuses 
Overall, we are here to have some fun.

## Slide 4: Let’s first remind ourselves… and learn something new

## Slide 5: Boolean logic
1
0
X
Z

## Slide 6: Boolean operations
AND
OR
XOR
NOT
NAND
NOR
XNOR
INPUT |  | OUTPUT |  |  |  |  | 
A | B | A AND B | A NAND B | A OR B | A NOR B | A NOR B | A XNOR B
0 | 0 | 0 | 1 | 0 | 1 | 0 | 1
0 | 1 | 0 | 1 | 1 | 0 | 1 | 0
1 | 0 | 0 | 1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 0 | 1 | 0 | 0 | 1

## Slide 7: D Flip-Flop
CLK | D | R | S | Q | !Q
rising edge | 0 | 0 | 0 | 0 | 1
rising edge | 1 | 0 | 0 | 1 | 0
falling edge | x | 0 | 0 | Q | !Q
x | x | 1 | 0 | 0 | 1
x | x | 0 | 1 | 1 | 0
x | x | 1 | 1 | 1 | 1
D
CLK
Q
!Q
CLK
Rising edge
Falling edge

## Slide 8: What is FPGA ?
Field-programmable gate array
Logic block – LUT + D Flip-Flop + full adder
I/O block – one per each pin
Interconnections, clock tree
Hard block – Block RAM, multipliers, DSP, CPU,…
Vendors: Xilinx, Intel/Altera, Lattice, Microsemi …

## Slide 9: Logic block
LUT
Full
Adder
MUX
MUX
MUX
D
Flip-Flop
Clock
Carry in
Carry out
Input
Output

## Slide 10: How do we program FPGA ?
HDL - Hardware description language
VHDL and Verilog
Analysis: parsing and validation of HDL
Synthesis: HDL -> netlist
Place-and-route: netlist -> specific FPGA technology
Assembler: specific FPGA technology -> bitstream
Programming: deploying bitstream on device (serial flash memory or directly)
Timing analysis
Simulation

## Slide 11: Open source tools
Yosys - Verilog synthesis tool by Clifford Wolf
Arachne PnR - Place and route tool by Cotton Seed
Project IceStorm – Assembler, time analysis and FPGA programming tool
by Clifford Wolf and Mathias Lasser
Lattice iCE40 FPGA only
Icarus Verilog by Stephen Williams
Verilator by Wilson Snyder with Duane Galbi and Paul Wasson

## Slide 12: And more…
APIO – micro-ecosystem for open FPGAs by Jesús Arroyo Torrens and Juan González (Obijuan)
FuseSoC - package manager and a set of build tools for FPGA/ASIC development by Olof Kindgren
Icestudio - graphic editor for open FPGAs by Jesús Arroyo Torrens

## Slide 13: Let’s get started

## Slide 14: What does computer consists of ?
CPU
  Registers
  ALU - Arithmetic logic unit
  Control unit
Memory
I/O devices
How do we name our project ?

## Slide 15: Grom-8
Simple
Not lightning fast
Thunder is always slower
Polish word is GROM
And we will put 8 in name, since it is 8 bit

## Slide 16: Architecture
8 bit CPU
4 general purpose registers
12 bit address bus and PC (program counter)
Code and data segment registers (CS,DS) (4 bit)
Stack pointer (SP) (12 bit)
8-bit ALU with C-carry, Z-zero and S-sign flags

## Slide 17: Instruction set 1/2
IR |  |  | 2nd | Instruction | Info
0000 | dst | src |  | MOV dst, src | 
0001 | 00 | reg |  | ADD reg | r0 = r0 + reg
0001 | 01 | reg |  | SUB reg | r0 = r0 - reg
0001 | 10 | reg |  | ADC reg | r0 = r0 + reg + C
0001 | 11 | reg |  | SBC reg | r0 = r0 - reg - C
0010 | 00 | reg |  | AND reg | r0 = r0 and reg
0010 | 01 | reg |  | OR reg | r0 = r0 or reg
0010 | 10 | reg |  | NOT reg | r0 = not reg
0010 | 11 | reg |  | XOR reg | r0 = r0 xor reg
0011 | 00 | reg |  | INC reg | reg = reg + 1
0011 | 01 | reg |  | DEC reg | reg = reg - 1
0011 | 10 | reg |  | CMP reg | flags of r0 - reg
0011 | 11 | reg |  | TST reg | flags of r0 and reg
0100 | 00 | 00 |  | SHL | 
0100 | 00 | 01 |  | SHR | 
0100 | 00 | 10 |  | SAL | 
0100 | 00 | 11 |  | SAR | 
0100 | 01 | 00 |  | ROL | 
0100 | 01 | 01 |  | ROR | 
0100 | 01 | 10 |  | RCL | rotate with carry
0100 | 01 | 11 |  | RCR | rotate with carry
0100 | 10 | reg |  | PUSH reg | 
0100 | 11 | reg |  | POP reg | 
0101 | dst | src |  | LOAD dst, [src] | 
0110 | dst | src |  | STORE [dst], src | 
0111 | 00 | reg |  | MOV CS, reg | 
0111 | 01 | reg |  | MOV DS, reg | 
0111 | 10 | 00 |  | PUSH CS | 
0111 | 10 | 01 |  | PUSH DS | 
0111 | 10 | 10 |  | ??? | 
0111 | 10 | 11 |  | ??? | 
0111 | 11 | 00 |  | ??? | 
0111 | 11 | 01 |  | ??? | 
0111 | 11 | 10 |  | RET | 
0111 | 11 | 11 |  | HLT | 

## Slide 18: Instruction set 2/2
1000 | 00 | 00 | val | JMP val | (unconditionally jump)
1000 | 00 | 01 | val | JC val | (carry=1 jump)
1000 | 00 | 10 | val | JNC val | (carry=0 jump)
1000 | 00 | 11 | val | JM val | (sign=1 jump)
1000 | 01 | 00 | val | JP val | (sign=0 jump)
1000 | 01 | 01 | val | JZ val | (zero=1 jump)
1000 | 01 | 10 | val | JNZ val | (zero=0 jump)
1000 | 01 | 11 | val | ??? | 
1000 | 10 | 00 | val | JR val | (unconditionally jump)
1000 | 10 | 01 | val | JRC val | (carry=1 jump)
1000 | 10 | 10 | val | JRNC val | (carry=0 jump)
1000 | 10 | 11 | val | JRM val | (sign=1 jump)
1000 | 11 | 00 | val | JRP val | (sign=0 jump)
1000 | 11 | 01 | val | JRZ val | (zero=1 jump)
1000 | 11 | 10 | val | JRNZ val | (zero=0 jump)
1000 | 11 | 11 | val | ??? | 
1001 | high |  | low | JUMP addr | 
1010 | high |  | low | CALL addr | 
1011 | high |  | low | MOV SP,addr | 
1100 | xx | reg | val | IN reg,[val] | 
1101 | xx | reg | val | OUT [val],reg | 
1110 | xx | 00 | val | MOV CS,val | 
1110 | xx | 01 | val | MOV DS,val | 
1110 | xx | 10 | val | ??? | 
1110 | xx | 11 | val | ??? | 
1111 | 00 | reg | val | MOV reg, val | 
1111 | 01 | reg | val | LOAD reg, [val] | 
1111 | 10 | reg | val | STORE [val], reg | 
1111 | 11 | xx |  | ??? | 

## Slide 19: Verilog

## Slide 20: Memory

## Slide 21: Modules
module ram_memory(
input clk,
input [11:0] addr,
input [7:0] data_in,
input we,
output reg [7:0] data_out
);
reg [7:0] store[0:4095]
initial
begin
$readmemh("boot.mem", store);
end
always @(posedge clk)
if (we)
store[addr] <= data_in;
else
data_out <= store[addr];
endmodule

## Slide 22: Inputs and outputs
module ram_memory(
input clk,
input [11:0] addr,
input [7:0] data_in,
input we,
output reg [7:0] data_out
);
reg [7:0] store[0:4095]
initial
begin
$readmemh("boot.mem", store);
end
always @(posedge clk)
if (we)
store[addr] <= data_in;
else
data_out <= store[addr];
endmodule

## Slide 23: Registers
module ram_memory(
input clk,
input [11:0] addr,
input [7:0] data_in,
input we,
output reg [7:0] data_out
);
reg [7:0] store[0:4095];
initial
begin
$readmemh("boot.mem", store);
end
always @(posedge clk)
if (we)
store[addr] <= data_in;
else
data_out <= store[addr];
endmodule

## Slide 24: Initial block
module ram_memory(
input clk,
input [11:0] addr,
input [7:0] data_in,
input we,
output reg [7:0] data_out
);
reg [7:0] store[0:4095];
initial
begin
$readmemh("boot.mem", store);
end
always @(posedge clk)
if (we)
store[addr] <= data_in;
else
data_out <= store[addr];
endmodule

## Slide 25: Always block
module ram_memory(
input clk,
input [11:0] addr,
input [7:0] data_in,
input we,
output reg [7:0] data_out
);
reg [7:0] store[0:4095];
initial
begin
$readmemh("boot.mem", store);
end
always @(posedge clk)
if (we)
store[addr] <= data_in;
else
data_out <= store[addr];
endmodule

## Slide 26: Condition check
module ram_memory(
input clk,
input [11:0] addr,
input [7:0] data_in,
input we,
output reg [7:0] data_out
);
reg [7:0] store[0:4095];
initial
begin
$readmemh("boot.mem", store);
end
always @(posedge clk)
if (we)
store[addr] <= data_in;
else
data_out <= store[addr];
endmodule

## Slide 27: Non-blocking assignment
module ram_memory(
input clk,
input [11:0] addr,
input [7:0] data_in,
input we,
output reg [7:0] data_out
);
reg [7:0] store[0:4095];
initial
begin
$readmemh("boot.mem", store);
end
always @(posedge clk)
if (we)
store[addr] <= data_in;
else
data_out <= store[addr];
endmodule

## Slide 28: Parallel execution
addr <= PC;
PC <= PC + 1;
SAME
PC <= PC + 1;
addr <= PC;
addr = PC;
PC = PC + 1;
NOT SAME
PC = PC + 1;
addr = PC;

## Slide 29: I/O devices

## Slide 30: Begin – end block
module hex_to_7seg
(
input [3:0] i_Value,
// ...
output o_Segment_G
);
reg [6:0] out = 7'b0000000;
always @(posedge i_Clk)
begin
case (i_Value)
4'b0000 : out <= 7'b0000001;
4'b0001 : out <= 7'b1001111;
// ...
4'b1110 : out <= 7'b0110000;
4'b1111 : out <= 7'b0111000;
endcase
end
assign o_Segment_A = out[6];
// ...
endmodule

## Slide 31: Case
module hex_to_7seg
(
input [3:0] i_Value,
// ...
output o_Segment_G
);
reg [6:0] out = 7'b0000000;
always @(posedge i_Clk)
begin
case (i_Value)
4'b0000 : out <= 7'b0000001;
4'b0001 : out <= 7'b1001111;
// ...
4'b1110 : out <= 7'b0110000;
4'b1111 : out <= 7'b0111000;
endcase
end
assign o_Segment_A = out[6];
// ...
endmodule

## Slide 32: Continuous assignment
module hex_to_7seg
(
input [3:0] i_Value,
// ...
output o_Segment_G
);
reg [6:0] out = 7'b0000000;
always @(posedge i_Clk)
begin
case (i_Value)
4'b0000 : out <= 7'b0000001;
4'b0001 : out <= 7'b1001111;
// ...
4'b1110 : out <= 7'b0110000;
4'b1111 : out <= 7'b0111000;
endcase
end
assign o_Segment_A = out[6];
// ...
endmodule

## Slide 33: ALU

## Slide 34: Local parameters / Constants
module alu(
input clk,
input [7:0] A,
input [7:0] B,
input [3:0] operation,
output reg [7:0] result,
output reg CF,
output reg ZF,
output reg SF
);
localparam ALU_OP_ADD = 4'b0000;
localparam ALU_OP_SUB = 4'b0001;
//...
localparam ALU_OP_RCR = 4'b1111;
reg [8:0] tmp;
always @(posedge clk)
begin
case (operation)
ALU_OP_ADD :
tmp = A + B;

## Slide 35: Blocking assignment
reg [8:0] tmp;
case (operation)
ALU_OP_ADD :
tmp = A + B;
ALU_OP_SUB :
tmp = A - B;
ALU_OP_ADC :
tmp = A + B + { 7'b0000000, CF };
ALU_OP_SBC :
tmp = A - B - { 7'b0000000, CF };
// ...
endcase
CF <= tmp[8];
ZF <= tmp[7:0] == 0;
SF <= tmp[7];
result <= tmp[7:0];

## Slide 36: ALU - Arithmetic operations
reg [8:0] tmp;
case (operation)
ALU_OP_ADD :
tmp = A + B;
ALU_OP_SUB :
tmp = A - B;
ALU_OP_ADC :
tmp = A + B + { 7'b0000000, CF };
ALU_OP_SBC :
tmp = A - B - { 7'b0000000, CF };
// ...
endcase
CF <= tmp[8];
ZF <= tmp[7:0] == 0;
SF <= tmp[7];
result <= tmp[7:0];

## Slide 37: ALU – Bitwise logic operations
reg [8:0] tmp;
case (operation)
// ...
ALU_OP_AND :
tmp = {1'b0, A & B };
ALU_OP_OR :
tmp = {1'b0, A | B };
ALU_OP_NOT :
tmp = {1'b0, ~B };
ALU_OP_XOR :
tmp = {1'b0, A ^ B};
// ...
endcase
CF <= tmp[8];
ZF <= tmp[7:0] == 0;
SF <= tmp[7];
result <= tmp[7:0];

## Slide 38: ALU - Shift operations
reg [8:0] tmp;
case (operation)
// ...
ALU_OP_SHL :
tmp = { A[7], A[6:0], 1'b0};
ALU_OP_SHR :
tmp = { A[0], 1'b0, A[7:1]};
ALU_OP_SAL :
tmp = { A[7], A[6:0], 1'b0}; // Same as SHL
ALU_OP_SAR :
tmp = { A[0], A[7], A[7:1]};
// ...
endcase
CF <= tmp[8];
ZF <= tmp[7:0] == 0;
SF <= tmp[7];
result <= tmp[7:0];

## Slide 39: ALU - Rotate operations
reg [8:0] tmp;
case (operation)
// ...
ALU_OP_ROL :
tmp = { A[7], A[6:0], A[7]};
ALU_OP_ROR :
tmp = { A[0], A[0], A[7:1]};
ALU_OP_RCL :
tmp = { A[7], A[6:0], CF};
ALU_OP_RCR :
tmp = { A[0], CF, A[7:1]};
// ...
endcase
CF <= tmp[8];
ZF <= tmp[7:0] == 0;
SF <= tmp[7];
result <= tmp[7:0];

## Slide 40: ALU – Flags and result
reg [8:0] tmp;
case (operation)
// ...
ALU_OP_ROL :
tmp = { A[7], A[6:0], A[7]};
ALU_OP_ROR :
tmp = { A[0], A[0], A[7:1]};
ALU_OP_RCL :
tmp = { A[7], A[6:0], CF};
ALU_OP_RCR :
tmp = { A[0], CF, A[7:1]};
// ...
endcase
CF <= tmp[8];
ZF <= tmp[7:0] == 0;
SF <= tmp[7];
result <= tmp[7:0];

## Slide 41: Other operations
Multiply
{R[1],R[0]} <= R[0] * R[1];
Divide
R[0] <= R[0] / R[1];
Modulus
R[0] <= R[0] % R[1];
Shift left by 1 (multiply by 2)
R[0] <= R[0] << 1;
Shift right by 1 (divide by 2)
R[0] <= R[0] >> 1;

## Slide 42: CPU

## Slide 43: Wires
module grom_cpu(
input clk,input reset,
output reg [11:0] addr,
input [7:0] data_in,output reg [7:0] data_out,
output reg we,output reg ioreq, output reg hlt
);
reg[11:0] PC; // Program counter
reg[7:0] IR; // Instruction register
reg[11:0] SP; // Stack pointer regiser
reg[7:0] R[0:3]; // General purpose registers
// ...
reg [7:0] alu_a;
reg [7:0] alu_b;
reg [3:0] alu_op;
wire [7:0] alu_res;
wire alu_CF;
wire alu_ZF;
wire alu_SF;
alu alu(.clk(clk),.A(alu_a),.B(alu_b),.operation(alu_op),
.result(alu_res),.CF(alu_CF),.ZF(alu_ZF),.SF(alu_SF));
// ...

## Slide 44: Using modules
module grom_cpu(
input clk,input reset,
output reg [11:0] addr,
input [7:0] data_in,output reg [7:0] data_out,
output reg we,output reg ioreq, output reg hlt
);
reg[11:0] PC; // Program counter
reg[7:0] IR; // Instruction register
reg[11:0] SP; // Stack pointer regiser
reg[7:0] R[0:3]; // General purpose registers
// ...
reg [7:0] alu_a;
reg [7:0] alu_b;
reg [3:0] alu_op;
wire [7:0] alu_res;
wire alu_CF;
wire alu_ZF;
wire alu_SF;
alu alu(.clk(clk),.A(alu_a),.B(alu_b),.operation(alu_op),
.result(alu_res),.CF(alu_CF),.ZF(alu_ZF),.SF(alu_SF));
// ...

## Slide 45: Main state machine
reg [4:0] state = STATE_RESET;
always @(posedge clk)
begin
if (reset)
begin
state <= STATE_RESET;
hlt <= 0;
end
else
begin
case (state)
STATE_RESET :
begin
PC <= 12'h000;
R[0] <= 8'h00;
// ...
SP <= 12'hfff;
state <= STATE_FETCH_PREP;
end

## Slide 46: Instruction fetch
STATE_FETCH_PREP :
begin
addr <= PC;
we <= 0;
ioreq <= 0;
state <= STATE_FETCH_WAIT;
end
STATE_FETCH_WAIT :
begin
// Sync with memory due to CLK
state <= (hlt) ? STATE_FETCH_PREP : STATE_FETCH;
end
STATE_FETCH :
begin
IR <= data_in;
PC <= PC + 1;
state <= STATE_EXECUTE;
end

## Slide 47: Instruction decoding
STATE_EXECUTE :
begin
if (IR[7])
begin
addr <= PC;
state <= STATE_FETCH_VALUE_PREP;
PC <= PC + 1;
end
else
begin
case(IR[6:4])
3'b000 :
begin
`ifdef DISASSEMBLY
$display("MOV R%d,R%d",IR[3:2],IR[1:0]);
`endif
R[IR[3:2]] <= R[IR[1:0]];
state <= STATE_FETCH_PREP;
end

## Slide 48: MOV instruction
STATE_EXECUTE :
begin
if (IR[7])
begin
addr <= PC;
state <= STATE_FETCH_VALUE_PREP;
PC <= PC + 1;
end
else
begin
case(IR[6:4])
3'b000 :
begin
`ifdef DISASSEMBLY
$display("MOV R%d,R%d",IR[3:2],IR[1:0]);
`endif
R[IR[3:2]] <= R[IR[1:0]];
state <= STATE_FETCH_PREP;
end

## Slide 49: Conditional compiling
STATE_EXECUTE :
begin
if (IR[7])
begin
addr <= PC;
state <= STATE_FETCH_VALUE_PREP;
PC <= PC + 1;
end
else
begin
case(IR[6:4])
3'b000 :
begin
`ifdef DISASSEMBLY
$display("MOV R%d,R%d",IR[3:2],IR[1:0]);
`endif
R[IR[3:2]] <= R[IR[1:0]];
state <= STATE_FETCH_PREP;
end

## Slide 50: Using ALU module 1/2
3'b001 :
begin
alu_a <= R[0]; // first input R0
alu_b <= R[IR[1:0]];
RESULT_REG <= 0; // result in R0
alu_op <= { 2'b00, IR[3:2] };
state <= STATE_ALU_RESULT_WAIT;
end
3'b010 :
begin
alu_a <= R[0]; // first input R0
alu_b <= R[IR[1:0]];
RESULT_REG <= 0; // result in R0
alu_op <= { 2'b01, IR[3:2] };
state <= STATE_ALU_RESULT_WAIT;
end

## Slide 51: Using ALU module 2/2
STATE_ALU_RESULT_WAIT :
begin
state <= STATE_ALU_RESULT;
end
STATE_ALU_RESULT :
begin
R[RESULT_REG] <= alu_res;
state <= STATE_FETCH_PREP;
end

## Slide 52: Memory operations 1/2
3'b101 :
begin
`ifdef DISASSEMBLY
$display("LOAD R%d,[R%d]", IR[3:2], IR[1:0]);
`endif
addr <= { DS, R[IR[1:0]] };
we <= 0;
ioreq <= 0;
RESULT_REG <= IR[3:2];
state <= STATE_LOAD_VALUE_WAIT;
end
3'b110 :
begin
`ifdef DISASSEMBLY
$display("STORE [R%d],R%d", IR[3:2], IR[1:0]);
`endif
addr <= { DS, R[IR[3:2]] };
we <= 1;
ioreq <= 0;
data_out <= R[IR[1:0]];
state <= STATE_FETCH_PREP;
end

## Slide 53: Memory operations 2/2
STATE_LOAD_VALUE_WAIT :
begin
// Sync with memory due to CLK
state <= STATE_LOAD_VALUE;
end
STATE_LOAD_VALUE :
begin
R[RESULT_REG] <= data_in;
we <= 0;
state <= STATE_FETCH_PREP;
end

## Slide 54: Computer

## Slide 55: Main implementation
module grom_computer(input clk,input reset,output hlt,output reg[7:0] display_out );
wire [11:0] addr;
wire [7:0] memory_out;
wire [7:0] memory_in;
wire mem_enable;
wire we;
wire ioreq;
grom_cpu cpu(.clk(clk),.reset(reset),.addr(addr),.data_in(memory_out),
.data_out(memory_in),.we(we),.ioreq(ioreq),.hlt(hlt));
assign mem_enable = we & ~ioreq;
ram_memory memory(.clk(clk),.addr(addr),.data_in(memory_in),
.we(mem_enable),.data_out(memory_out));
always @(posedge clk)
begin
if(ioreq==1 && we==1)
begin
display_out <= memory_in;
end
end
endmodule

## Slide 56: Icestudio

## Slide 57: Simulation

## Slide 58: Test program
store[0] <= 8'b11100001; // MOV DS,2
store[1] <= 8'b00000010; //
store[2] <= 8'b01010100; // LOAD R1,[R0]
store[3] <= 8'b00110001; // INC R1
store[4] <= 8'b00110001; // INC R1
store[5] <= 8'b01100001; // STORE [R0],R1
store[6] <= 8'b11010001; // OUT [0],R1
store[7] <= 8'b00000000; //
store[8] <= 8'b00110001; // INC R1
store[9] <= 8'b10100001; // CALL 0x100
store[10] <= 8'b00000000; //
store[11] <= 8'b01111111; // HLT
store[256] <= 8'b11010001; // OUT [0],R1
store[257] <= 8'b00000000; //
store[258] <= 8'b01111110; // RET

## Slide 59: Test bench
`timescale 1ns/1ps
module grom_computer_tb();
reg clk = 0;
reg reset;
wire [7:0] display_out;
wire hlt;
grom_computer computer(.clk(clk),.reset(reset),.hlt(hlt),.display_out(display_out));
always
#(5) clk <= !clk;
initial
begin
$dumpfile("grom_computer_tb.vcd");
$dumpvars(0,grom_computer_tb);
reset = 1;
#20
reset = 0;
#900
$finish;
end
endmodule

## Slide 61: Text output
iverilog -D DISASSEMBLY -o grom.out grom_computer_tb.v ram_memory.v alu.v grom_cpu.v grom_computer.v
vvp grom.out
VCD info: dumpfile grom_computer_tb.vcd opened for output.
PC 001 R0 00 R1 00 R2 00 R3 00 CS 0 DS 0 SP fff ALU [x x x]
MOV DS,0x02
PC 003 R0 00 R1 00 R2 00 R3 00 CS 0 DS 2 SP fff ALU [x x x]
LOAD R1,[R0]
PC 004 R0 00 R1 00 R2 00 R3 00 CS 0 DS 2 SP fff ALU [x x x]
INC R1
PC 005 R0 00 R1 01 R2 00 R3 00 CS 0 DS 2 SP fff ALU [0 0 0]
INC R1
PC 006 R0 00 R1 02 R2 00 R3 00 CS 0 DS 2 SP fff ALU [0 0 0]
STORE [R0],R1
PC 007 R0 00 R1 02 R2 00 R3 00 CS 0 DS 2 SP fff ALU [0 0 0]
OUT [0x00],R1
Display output : 02
PC 009 R0 00 R1 02 R2 00 R3 00 CS 0 DS 2 SP fff ALU [0 0 0]
INC R1
PC 00a R0 00 R1 03 R2 00 R3 00 CS 0 DS 2 SP fff ALU [0 0 0]
CALL 100
Jumping to 100
PC 101 R0 00 R1 03 R2 00 R3 00 CS 0 DS 2 SP ffd ALU [0 0 0]
OUT [0x00],R1
Display output : 03
PC 103 R0 00 R1 03 R2 00 R3 00 CS 0 DS 2 SP ffd ALU [0 0 0]
RET
Jumping to 00b
PC 00c R0 00 R1 03 R2 00 R3 00 CS 0 DS 2 SP fff ALU [0 0 0]
HALT

## Slide 62: Unit testing

## Slide 63: C++ for testing 1/2
#include <iostream>
#include <memory>
#include "Valu.h"
#include "verilated.h"
#define CATCH_CONFIG_RUNNER
#include "catch.hpp"
int main( int argc, char* argv[] )
{
Verilated::commandArgs(argc, argv);
int result = Catch::Session().run( argc, argv );
return ( result < 0xff ? result : 0xff );
}

## Slide 64: C++ for testing 2/2
TEST_CASE("Test ALU_OP_ADD", "ALU")
{
std::unique_ptr<Valu> top = std::make_unique<Valu>();
top->clk = 0;
for(int A=0;A<0x100;A++)
{
for(int B=0;B<0x100;B++)
{
top->A = A;
top->B = B;
top->operation = top->alu__DOT__ALU_OP_ADD;
top->clk ^= 1; top->eval();
top->clk ^= 1; top->eval();
uint8_t res = A + B;
REQUIRE(res==top->result);
REQUIRE(((res==0) ? 1:0)==top->ZF);
REQUIRE((((A + B)>0xff) ? 1 : 0 )==top->CF);
REQUIRE(((res & 0x80) ? 1 : 0) == top->SF);
}
}
}

## Slide 65: Real hardware

## Slide 66: Connecting with hardware
module grom_top
(input i_Clk, // Main Clock
input i_Switch_1, // SW1 button
output o_Segment1_A,
// ...
output o_Segment2_G
);
wire [7:0] display_out;
wire hlt;
grom_computer computer(.clk(i_Clk),.reset(i_Switch_1),.hlt(hlt),.display_out(display_out));
hex_to_7seg upper_digit
(.i_Clk(i_Clk),.i_Value(display_out[7:4]),
.o_Segment_A(o_Segment1_A),.o_Segment_B(o_Segment1_B),.o_Segment_C(o_Segment1_C),
.o_Segment_D(o_Segment1_D),.o_Segment_E(o_Segment1_E),.o_Segment_F(o_Segment1_F),
.o_Segment_G(o_Segment1_G));
hex_to_7seg lower_digit
(.i_Clk(i_Clk),.i_Value(display_out[3:0]),
.o_Segment_A(o_Segment2_A),.o_Segment_B(o_Segment2_B),.o_Segment_C(o_Segment2_C),
.o_Segment_D(o_Segment2_D),.o_Segment_E(o_Segment2_E),.o_Segment_F(o_Segment2_F),
.o_Segment_G(o_Segment2_G));
endmodule

## Slide 67: Board definition file
### Main FPGA Clock
set_io i_Clk 15
## Push-Button Switches
set_io i_Switch_1 53
### LED Pins:
set_io o_LED_1 56
set_io o_LED_2 57
set_io o_LED_3 59
set_io o_LED_4 60
### 7 Segment Outputs
set_io o_Segment1_A 3
set_io o_Segment1_B 4
...
set_io o_Segment2_C 97
set_io o_Segment2_D 95
set_io o_Segment2_E 94
set_io o_Segment2_F 8
set_io o_Segment2_G 96

## Slide 68: Go Board

## Slide 69: Live demo

## Slide 70: The End

## Slide 71: More info
Full source code at https://github.com/mmicko/grom8
Nandland YouTube video channel
http://www.fpga4student.com/ for beginner tutorials
http://www.clifford.at/yosys/ for those interested in open source tools

## Slide 72: Q & A